## Slide 1: Perceiving Internet Anomalies via CDN Replica Shifts Tsinghua University Northwestern University
Yihao Jia, Aleksandar Kuzmanovic
INFOCOM’19 Paris

## Slide 2: network anomalies CDN replica shift
Side A
Side B

## Slide 3: The Challenge of internet anomalies perception Timely anomaly alert Sophisticated measurement
internet anomalies detection involves measurements
real-time perception involves real-time measurements
real-time measurement is complicated
maintaining a real-time measurement system is costly

## Slide 4
CDN replica assignments imply...

## Slide 5: Why CDN replica assignments imply anomalies
CDN provides users with high QoS by extensive replicas
occasional network anomaly is a common event that degrade QoS
CDN re-assign replicas when anomalies hit the QoS

## Slide 6: Replica assignment <> Anomalies Anomalies dodge build CDN Network
Sophisticated
meaurement system
QoS
replica assignment
network anomalies

## Slide 7: Detecting network anomalies
by observing CDN replica assignments
detect anomaly events in statistical terms
as a “whistle-blower” to trigger sophisticated measurements
practically

## Slide 8: Content
Why replica shift…
How to observe the shift...
How replica shift...
Anomalies behind shifts…
Case study…
Conclusion...

## Slide 9: How CDN control replica assignment (Background) Anycast-based CDN DNS-based CDN
user direction is naturally handled by the BGP
uncontrollable
self-controllable

## Slide 10: How replica shifts imply anomalies?
INSIDER
internal
external
OUTSIDER
conventional
exceptional

## Slide 11: What drives a replica shift?

## Slide 12: The exceptional shifts Regional shifts Occasional shifts
if the users are mapped to
a different region
than the one they reside in
Spatially exceptional
Temporally exceptional
if the users are mapped to
an “alien” replica
that rarely, if ever, showed up for the particular users.

## Slide 13: Content
Why replica shift…
How to observe the shift...
How replica shift...
Anomalies behind shifts…
Case study…
Conclusion...

## Slide 14: Focus on the DNS-based CDN Explore it as an Outsider Discover the DNS behavior of CDNs

## Slide 15: The ECS option (Background) What is ECS? The ECS prevalence Why ECS Valuable?
Elient Subnet Option: a DNS option that carry accurate user location
the prevalence of public DNS resolver
mapping accuracy (public resolver & Authoritative DNS)
DNS behavior can be remotely monitored from a single machine

## Slide 16: How we measure What CDN should we choose? Which domain we select for each CDN?
DNS-based, ECS enable
using ECS option to carry IP of any networks
Domains that CONSTANTLY serve abundant trafﬁc

## Slide 17
 | Domain | ECS enable? | How we measure?
Akamai | apple.com | No | 1000 U.S. public resolvers
Google Cloud | android.com | Yes | 1 Self-built resolvers (ECS-enable) [1000 public resolver IPs]
Fastly | imgur.com |  | 
Incapsula | t-mobile.com |  | 
Cloudfront | zillow.com |  | 

## Slide 18: Content
Why replica shift…
How to observe the shift...
How replica shift...
Anomalies behind shifts…
Case study…
Conclusion...

## Slide 19: How to claim the shift... 5.5.5.5 5.5.10.5 5.5.5.10 replica assigned to another cluster replica’s IPs vary beyond the /24 space
/24 is the longest preﬁx that can be routed by BGP
shifts within the same /24 reside in the same cluster, and share the same routes
Shift
Notes: This, to a large extent, helps us to ﬁltering the shifts residing in the same cluster, which is probably not triggered by anomalies.

## Slide 20: Replica shift frequency
Google>Akamai>Amazon>Fastly>Incapsula
Dampling rate: 20s
Data period: Jun. 2018
Frequency
Dynamism
Akamai & Amazon shift more frequently during daytime than overnight

## Slide 21: Regular replica quantity across networks
Google, Akamai, Amazon show an afﬂuent quantity in assigning replicas to networks, far beyond that in Incapsula and Fastly

## Slide 22: How to claim the exceptional shift... 2. For a speciﬁc network, if a returned replica that outside the base, we call it the exception shift For any kind of exceptional shift, we collect it’s base replica

## Slide 23: How to claim the exceptional shift...
reginal shift
Occasional shifts
replicas that collected in U.S., Canada, Mexico
a new replica that outside the base
replicas that collected in June

## Slide 24: Frequency of occurrence: exceptional shifts
Evaluating phase: July 15 to 22, 2018
Both regional shifts and occasional shifts are rare among all CDNs
Google and Amazon show no regional shifts
Incapsula and Fastly rarely show regional and occasional shifts relative to others

## Slide 25: Content
Why replica shift…
How to observe the shift...
How replica shift...
Anomalies behind shifts…
Case study…
Conclusion...

## Slide 26: How to understand the anomalies?
Latency

## Slide 27: Probe Network

## Slide 28: Probe Network
Find the maximal Δ
exceptional shift
alert
probing

## Slide 29: CDF of regional shifts on ∆value Akamai: Incapsula & Fastly:
a weak indication for anomalies
a clear indication for anomalies
Medain case

## Slide 30: CDF of occasional shifts on ∆value
All CDNs present a relatively weak indication
Medain case

## Slide 31: Distribution of ∆ratio (inflation) Akamai: Incapsula & Fastly:
a weak indication for anomalies on regional shift
a strong indication for anomalies on regional shift

## Slide 32: Content
Why replica shift…
How to observe the shift...
How replica shift...
Anomalies behind shifts…
Case study…
Conclusion...

## Slide 33: Exceptional shift alert alert alert alert Warning
Detection via Multi-CDN
!
!
!
CDN-1
CDN-2
CDN-3

## Slide 34: An anomaly case: routing detour Content Service time: 0 ms

## Slide 35: An anomaly case: routing detour Content Service time: 80(40*2) ms

## Slide 36: An anomaly case: routing detour Content Service time: 40 ms

## Slide 37: 80(40*2) ms

## Slide 38: Content
Why replica shift…
How to observe the shift...
How replica shift...
Anomalies behind shifts…
Case study…
Conclusion...

## Slide 39: Insights
[Unexpectedly] Incapsula and Fastly are almost perfectly suited
least number of replica shifts
lowest quantity of replica in their base
smallest frequency of exceptional shifts
shifts strongly correlated with anomalies

## Slide 40: Insights (Contd.)
Regional shifts are more correlated with anomalies than occasional shifts are.
[Counter-intuitively] replica shift by Akamai, Google, and Amazon are too sophisticated to be used to flag anomalies
Multiple CDNs concurrently exhibit an exceptional shift almost surely imply Internet anomalies.

## Slide 41: SUMMARY
propose a methodology to perceive anomalies via CDN replica shifts.
Explore the factors and ingredients that contribute to the shifts and anomalies detection.
Study the accuracy and promptness of the most popular CDNs in anomaly resilience.
Validate the feasibility of the proposed methodology by predicting anomalies in an authentic network environment.
Notes: This, to a large extent, helps us to ﬁltering the shifts residing in the same cluster, which is probably not triggered by anomalies.

## Slide 42: Qustions & Comments Thank You!
INFOCOM’19 Paris

## Slide 43: Backup slides...
Q&A
Notes: it is not very clear about what an Internet Anomaly actually is.
Is this methodology works in other country? - Europe?
CDN may shift differently among different domains.
What would anycast CDN do when anomalies happen?
if the proposed method fails to work on the biggest CDNs, the proposed approach may be limited.

## Slide 44: Is methodology works in Europe? For any kind of exceptional shift, we collect it’s base replica
exceptional shifts
base replicas

## Slide 45: May CDN shift differently among different domains? Yes Akamai design particular replica assignment model for different business. (static web content | streaming media | dynamic applications)

## Slide 46: What would anycast CDN do when anomalies happen? Mixed CDN, i.e., Microsoft, might be especial. (empowerd by both DNS and Anycast) Anycast CDN wouldn’t be controlled by CDN, but controlled by BGP itself.
“Fastroute: A scalable load-aware anycast routing architecture for modern CDNs,” Microsoft, 2015.